## Slide 1: Master Thesis
Prakhar Mehta
11th January 2019

## Slide 2: Agenda
Status
Hypothesis of problem and thesis title
Use of Netlogo or Python?
Discussion on model – individual and community
  ODD
Discussion on the go

## Slide 3: Status
CEA Tool
  Sample of 1637 ‘zones’ (simply referred to as buildings hereon)
    Demand data validated against literature – CEA model output data within appropriate range for residential buildings, need to check other building types against literature values
    19 different building types over 1637 buildings – concern for ABM?
      Different occupancies, sizes, electricity demands
    Photovoltaic tool gives PV output in kWh for every hour (need a quick check to see if the numbers are ok, they should be)

## Slide 4: Status Continued…
PV System ZEVs (Community Solar Regulations; EnergieSchweiz)
  30kW +  qualify for rebates under new law (Energy Act 2018)
  Yearly Demand 100 MWh+ (~30 households)  qualify for open electricity market
     consider 30kW < Community PV System Size < need to define a max system size
    Need to define minimum system size < Individual PV system size < 30 kW
  Making a community:
    At least one building must be adjacent to the building which installs the PV
    Merger cannot extend over public land (eg. roads) and private property if owner not part of ZEV
    Can't use distribution network
    All properties must be connected behind same grid connection point
    SIMPLE: we assume to create new ZEV (legal entity) – tenants + owner – can consider some fixed administrative costs
    Need to manually make communities due to so many restrictions!

## Slide 5: Individual v Community Solar
 | Individual Solar | Community Solar
Definition |  | 

## Slide 6: ABM
Muaafa: Very simple model, can include a lot more in it
  What time scale for the simulation? 10 years, 20 years?
    Yearly decision making or higher resolution?
  Population increase – if and how to include?
  Changing weather, demands, prices – how?
    CEA: only 1 weather file – need to ask if we can do more here!
  Agents’ attitudes
    Use historical prices/bills as some input to initial attitude of agent towards solar PV?
    How do these change? Use Theory of Planned behaviour ideology?
      TPB: attitudes formed by an individuals beliefs ( = initial attitude) about a behaviour and an evaluation of its outcomes ( = money savings, environmental impact)

## Slide 7: Hypothesis
With the new ZEV regulations in place, it makes more financial sense to install a (larger) community PV system to take advantage of the rebates.
Of course, community PV systems are more complicated:
  Legal procedure to form ZEV
  More coordination and communication needed; splitting shares and costs etc
Do ZEV regulations limit the optimal adoption of community PV systems?

## Slide 8: Scope

## Slide 9: What do I wish to find?
Differences in adoption levels:
  Community vs. Individual in terms of:
    Total installed capacity
    Geographical variability
    Greater per household system sizes in community
    Temporal variability in adoption
    Adoption variability with prices of PV, electricity, rebate levels, more relaxed description of what ZEV can be?

## Slide 10: Open Questions as of now
Household definition?
  Building data available: demand and number of people but not households
    Split demand into x households?
  Incomes for these households? – Statistics Office? Random distributions?
ABM
  Possible to build own model? Muaafa as blueprint?
  Software: Python seems best
  CEA number of buildings is 1637- will the ABM be meaningful then? Does identification of which building installed PV make sense given the limited random distribution possibilities?

## Slide 11: Next month
Jan Week 3: ODD for ABM, Make Communities
Jan Week 4: